## Slide 1: Introduction to Wireless Hacking
Josh Rabinowitz

## Slide 2: Course Agenda
Day 1 – Overview, Common Protocols
Day 2 – SDR, Tool Setup
Day 3 – Signal Capture, Protocol Deconstruction I
Day 4 – Protocol Deconstruction II, Replay Attacks
Day 5 – Transmission Synthesis, Jamming

## Slide 3: Day 1

## Slide 4: Day 1 Outline
Wireless Overview
Wireless Attacks
Common Protocols: Wi-Fi
Common Protocols: Zigbee
Other Common Protocols
Q&A

## Slide 5: Wireless Hacking: Advantages
There are countless advantages to attacking a target wirelessly, e.g.:
  Discretion
  Ease of access
  Common protocols
    Documented vulnerabilities
    Insecure configuration
    Commercial & open-source tools likely available
  Proprietary/generic protocols
    Reliant on security-through-obscurity
    Predictable or derivative implementations
  Wireless technology growing more abundant & changing rapidly

## Slide 6: Wireless Hacking: Disadvantages
Some drawbacks to wireless hacking include:
  Rapid change means outdated techniques, unmaintained tools (HW & SW)
  Learning curve
    Tool Development
    High-level fundamentals
      Networking, cryptography
    Low-level fundamentals
      E&M, RF Circuitry
      Analog & Digital Signal Processing
  Regulation/ Legal Risk

## Slide 7: Radio Spectrum
Note: There are various forms of “wireless” technology, such as:
  Optical
  Sonic
  EM Induction
  etc.
This course will deal with the most common form of wireless technology, radio waves.
The radio spectrum includes EM waves with frequencies from 3Hz to 3,000GHz (3THz).

## Slide 8: Radio Applications
RF communication is used in nearly every facet of modern life; wireless attacks may target:
  Cellular & Wi-Fi networks
  Sensor networks & home automation
  Wearables, connected health technology
  Consumer/Industrial appliances
  Automotive technology
  Short range – Remotes, keys, fobs, RFID, NFC
  Long range – Satellites, aerospace, weather balloons, etc.
  Much more…

## Slide 9: Networks by Spatial Scope
Nanoscale
Body (BAN)
Personal (PAN)
Local (LAN)
Campus (CAN)
Metropolitan (MAN)
Radio access (RAN)
Wide (WAN)

## Slide 10: IEEE 802 Family of Standards
Most protocols based on published standards:
802.11 – WLAN (Wi-Fi)
  802.11ah - LPWLAN
802.15 – WPAN
  802.15.1 – Bluetooth (unmaintained)
  802.15.4 – LPWPAN (Zigbee, Thread)
802.15.6 BAN

## Slide 11: Communication Protocols
“A communication protocol is a system of rules that allows two or more entities of a communications system to transmit information via any variation of a physical quantity. The protocol defines the rules, syntax, semantics, and synchronization of communication and possible error recovery methods. Protocols may be implemented by hardware, software, or a combination of both.”

## Slide 12: Communication Protocols
Implementations vary, but a typical protocol is based on:
  Strict, layered designs
  Formal specifications, Standard bodies
  Networks, topologies
  Data formats, addressing, routing
  Error detection; ACK’s, timeouts, retries
  Sequence/flow control, synchronization
Where protocols differ:
  RF characteristics – range, power, interference, etc.
  Published vs. proprietary design
  HW/SW implementation
  OSI layers covered
  Network Topology
  Applications

## Slide 13: Communication Protocols
Comparing by stack layers:

## Slide 14: Communication Protocols
Comparing by other metrics:

## Slide 15: Day 1 Outline
Wireless Overview
Wireless Attacks
Common Protocols: Wi-Fi
Common Protocols: Zigbee
Other Common Protocols
Q&A

## Slide 16: Basic Wireless Attacks
Wireless attacks come in many forms, often dependent on the specific technology
  Café Latte  Wi-Fi
  Bluesnarfing  Bluetooth
  Etc.
Most attacks involving wireless communication can be classified under three basic types:
  Sniffing: capturing wireless transmissions to understand/decode sensitive data
  Injection/Replay-based attacks: re-transmitting captured data (or synthesizing ad-hoc); includes hijacking, impersonation, IV attacks, etc.
  Jamming: Causing interference to prevent a successful transmission; essentially a DoS
Some attacks are a combination of these (e.g., the “Roll-Jam”, discussed later)

## Slide 17: RF Hacker’s Toolkit
Wireless Dongles
GNU Radio
SDR Receivers/Transmitters
Proprietary RF Modules & Software
RF Shielding Cage
Waveguides/Antennas
Python
  Scapy, Cryptography, Matplotlib, etc.
GQRX, Inspectrum, BinViz
Fuzzer-testers, protocol analyzers
Pineapple, Femtocell, etc.

## Slide 18: Attack Process
  Typical high-level approach:
Do we know the protocol in use?
Tool(s) available?
Run Attack
Develop Tool (if possible)
Identify or Deconstruct Protocol

## Slide 19: Attack Process
  For a common protocol with readymade tools, the ‘wireless’ part of an attack is relatively straightforward…
Do we know the protocol in use?
Tool(s) available?
Run Attack
Develop Tool (if possible)
Identify or Deconstruct Protocol

## Slide 20: Attack Process
  Examples:
(Protocol)
Wi-Fi
Bluetooth
Zigbee
Z-Wave
(SW; HW)
Aircrack-ng tool suite; external Wi-Fi adapter
‘Bluez’ stack; BT dongle
Killerbee platform; Apimote, RZ Raven
Killerzee, Zniffer; UZB3
Follow documentation
Run attack commands
(1)
(2)
(3)
(4)

## Slide 21: Day 1 Outline
Wireless Overview
Wireless Attacks
Common Protocols: Wi-Fi
Common Protocols: Zigbee
Other Common Protocols
Q&A

## Slide 22: Wi-Fi: Overview
Family of Wireless LANs based on IEEE 802.11 standard
Encryption: WEP, WPA (I/II/III)

## Slide 23: Wi-Fi: Common Attacks
Packet Sniffing
Cracking Encryption
Man-in-the-middle
Evil Twin/Wi-Phishing
Rogue AP
Spoofing
Café Latte
Denial-of-Service
Etc.

## Slide 24: Wi-Fi: Common Tools
Hardware:
  USB network adapter
Software:
  Wireshark – monitoring traffic
  Aircrack-ng – de-authentication, cracking & analysis
Other tools:
  Wi-Fi Pineapple – wireless auditing platform
  “Cantenna” – homemade directional waveguide
  Rogue AP’s
  Vulnerable/test routers

## Slide 25: Wireless Network Adapters
Pentest-friendly adapters (as of 2023):
  https://kalitut.com/usb-wi-fi-adapters-supporting-monitor/
Common chipsets:
  Atheros, Ralink, Realtek
Example: TP-Link TL-WN722N (~$30)
  Chipset: Atheros AR9271
  Standards: 802.11b, 802.11g, 802.11n
  Frequency range: 2400-2483.5 MHz
  Transmitter power: 20 dBm
  Antenna : removable omnidirectional antenna (RP- SMA)

## Slide 26: Aircrack-ng
Network software suite consisting of detector, packet sniffer, WEP and WPA/WPA2-PSK cracker
Most common tool for analyzing 802.11 wireless LANs
Works with any wireless adapter whose driver supports “Monitor Mode” (see next slide)
https://www.aircrack-ng.org/
Install with: “apt-get install aircrack-ng”

## Slide 27: Monitor Mode
Before attacking Wi-Fi networks, adapter must be in Monitor Mode
Normally, wireless card will check ethernet frames and discard unwanted packets
Monitor mode means our wireless card intercepts all traffic, regardless of association

## Slide 28: Monitor Mode
To start wireless interface in monitor mode:
Plug adapter into USB port
Use “iwconfig” to find interface
Notice Mode is “Managed” – we want this to say “Monitor”

## Slide 29: Monitor Mode
Next:
Kill blocker processes using “sudo airmon-ng check kill”
Note: this will turn off Linux network manager!
To turn back on: “sudo systemctl restart NetworkManager”

## Slide 30: Monitor Mode
Finally:
Run “sudo airmon-ng start [interface]”
Run “iwconfig” once more to check…

## Slide 31: Simple WEP Crack
Overview
  Basic WEP encryption: RC4 keystream XORed with plaintext
    40-bit key concatenated with 24-bit IV
    24 bits not enough to prevent repetition
  On busy network, takes minutes to crack
  Automated by tools such as Aircrack-ng

## Slide 32: Simple WEP Crack
Steps:
Test injection capability
Begin IV collection
Fake authentication with AP
Replay ARP requests
Crack key using IVs

## Slide 33: Simple WEP Crack
Step 1: Test injection capability
aireplay-ng -9 –e [AP name] –a [BSSID] [interface]
Determines whether we are close enough to AP for packet injection

## Slide 34: Simple WEP Crack
Step 2: Begin IV collection
airodump-ng –c [AP channel] –bssid [BSSID] –w [capture file] [interface]
Capture initialization vectors (IV’s) coming from target AP
(1st console)

## Slide 35: Simple WEP Crack
Step 3: Fake authentication with AP
aireplay-ng –1 0 –e [AP name] –a [BSSID] –h [interface address] [interface]
For injection to work, our MAC must be associated with the AP
(2nd console)

## Slide 36: Simple WEP Crack
Step 4: Replay ARP requests
aireplay-ng –3 –b [BSSID] –h [interface address] [interface]
Reinject ARP requests; AP will rebroadcast and generate new IV’s
(3rd console)

## Slide 37: Simple WEP Crack
Step 5: Crack key using IVs
aircrack-ng –b [BSSID] [capture file(s)]
Obtains WEP using IV’s gathered from previous steps
(3rd console)

## Slide 38: WPA/WPA2 Crack
Overview:
Unlike WEP, key is not static
Can crack pre-shared key using dictionary attack
Must first capture client handshake

## Slide 39: WPA/WPA2 Crack
Steps:
Collect authentication handshake
De-authenticate wireless client (optional)
Crack pre-shared key using authentication handshake

## Slide 40: WPA/WPA2 Crack
Step 1: Collect authentication handshake
airodump-ng –c [channel] –b [BSSID] –w [capture file] [interface]
Listen for 4-way handshake between client and target AP

## Slide 41: WPA/WPA2 Crack
Step 1: Collect authentication handshake
Handshake collected

## Slide 42: WPA/WPA2 Crack
Step 2: De-authenticate wireless client (optional)
aireplay-ng –0 1 –a [BSSID] –c [client to de-auth] [interface]
If needed, this will de-authenticate a client associated with the AP
By reauthenticating, they’ll generate the 4-way handshake we need
(2nd console)

## Slide 43: WPA/WPA2 Crack
Step 3: Crack pre-shared key using authentication handshake
aircrack-ng –w [password list] –b [BSSID] [capture file(s)]
Checks wordlist against captured handshake to obtain PSK

## Slide 44: Exercise
Goal: Use Aircrack-ng to crack Wi-Fi encryption
(Use either lab Wi-Fi or test router; should be provided with adaptor)
Install aircrack-ng suite
Plug in USB adapter & set in Monitor Mode
Determine test network encryption type (WEP, WPA, etc.)
Use aircrack-ng suite to obtain network key
  (Note: if using dictionary attack, create wordlist file containing network password)

## Slide 45: WPA/WPA2 vs. WPA3
WPA/WPA2 : Flaws | WPA/WPA2 |  | WPA3: Fixes
Protocols susceptible to off-line analysis | Weak passwords crackable w/Aircrack Suite | weak passwords crackable w/Aircrack Suite | Each PW guess requires interaction, placing temporal limit on attempts***
Lack of forward secrecy | PSK allows decryption of all associated traffic, future & past |  | SAE provides perfect forward secrecy; adversary w/password cannot recover earlier traffic, session keys, etc.
Group Temporal Key (GTK) vulnerabilities | “Hole196” | Authenticated attacker (possessing GTK) can perform MiTM or DoS | Implements client isolation to prevent using GTK
 | Insecure random number generator (RNG) | Quick GTK recovery, allows injection and unicast decryption | 
WPS PIN Recovery | Fairly quick password recovery | Fairly quick password recovery | Alternative configuration replaces WPS
“KRACK” Attack (Key Reinstallation) | Retransmit nonce in replay attack to obtain full keychain |  | Can’t hijack session w/out key (patches now prevent retransmitting nonce as well)
WPA3 – STILL vulnerable:
Rogue AP
Evil Twin
ARP Spoof
SSL Strip
DNS Spoof
DoS
***Downgrade & Side-Channel attacks
  e.g. “Dragonblood”
  Some vulnerabilities not patched for backward compatibility, e.g. hash-to-group function

## Slide 46: Attack Flow Diagram: WPA2-PSK

## Slide 47: Attack Flow Diagram: WPA3

## Slide 48: Day 1 Outline
Wireless Overview
Wireless Attacks
Common Protocols: Wi-Fi
Common Protocols: Zigbee
Other Common Protocols
Q&A

## Slide 49: Zigbee: Overview
Based on IEEE 802.15.4 specification for PAN
Low-power mesh networks for home automation, medical device data collection, etc.

## Slide 50: Zigbee: Overview
Stack layers:
(Note sub-GHz ISM band allocation varies by geography)

## Slide 51: Zigbee: Common Attacks
Packet Sniffing
Cracking Encryption
Replay
Tracking
Denial-of-Service
Application-level attacks
*Notice most threats are not unique to Zigbee

## Slide 52: Zigbee: Common Tools
Hardware:
  ApiMote by River Loop Security
  Atmel AVR RZ Raven
  Texas Instruments CC2531
Software:
  Killerbee
    https://github.com/riverloopsec/killerbee
    Complete toolkit; can be combined with Scapy to build custom tools (injectors, fuzzers, etc.)
  Bumblebee
    https://github.com/virtualabs/cc2531-killerbee-fw
    Killerbee-compatible firmware for TI CC2531
  ZigDiggity
    https://github.com/BishopFox/zigdiggity
    Limited toolkit; requires Raspbee shield + Raspi

## Slide 53: Killerbee
Framework for auditing Zigbee and IEEE 802.15.4 Networks
Installation:
(See https://github.com/riverloopsec/killerbee)

## Slide 54: Killerbee
Most important tools:
  zbid - Identifies available interfaces that can be used by KillerBee and associated tools.
  zbwireshark - Similar to zbdump but exposes a named pipe for real-time capture and viewing in Wireshark.
  zbdump - A tcpdump-like took to capture IEEE 802.15.4 frames to a libpcap or Daintree SNA packet capture file. Does not display real-time stats like tcpdump when not writing to a file.
  zbreplay - Implements a replay attack, reading from a specified Daintree DCF or libpcap packet capture file, retransmitting the frames. ACK frames are not retransmitted.
  zbstumbler - Active ZigBee and IEEE 802.15.4 network discovery tool. Zbstumbler sends beacon request frames out while channel hopping, recording and displaying summarized information about discovered devices. Can also log results to a CSV file.

## Slide 55: Exercise
Goal: Sniff traffic from Zigbee device using Killerbee tools
(Should be provided with Zigbee dongle & Bulb/Switch set)
Target Device: HEIMAN Smart Bulb & Dimmable Switch from Amazon
Pairing instructions:

## Slide 56: Exercise
Getting started:
  Plug dongle into USB port
  Use ‘zbid’ to list devices
  Find target device channel using ‘zbstumbler’
  See Man pages for help on command usage!
Things to try:
  Sniff/capture pairing process
  Sniff different commands from the remote
  Investigate in wireshark (‘zbwireshark’)
  Replay attacks using ‘zbreplay’

## Slide 57: Day 1 Outline
Wireless Overview
Wireless Attacks
Common Protocols: Wi-Fi
Common Protocols: Zigbee
Other Common Protocols
Q&A

## Slide 58: Other Common Protocols
Bluetooth/BLE Tools:
  BT dongle + Linuz ‘bluez’ stack
  Hcitool, gattool, wireshark
Z-Wave Tools:
  Dongle: ACC-UZB3-U-STA
  Software (by Silicon Labs):
    Z-Wave PC Programmer
    “Zniffer” Sniffing Utility
LoRa Tools:
  Dongle: Microchip RN2483, Pycom LoPy
  python-loranode

## Slide 59: Day 1 Outline
Wireless Overview
Wireless Attacks
Common Protocols: Wi-Fi
Common Protocols: Zigbee
Other Common Protocols
Q&A

## Slide 60: Day 2

## Slide 61: Day 2 Outline
Attack Process Revisited
Example: Garage Door
Example: Car Keys
Tool Setup
Q&A

## Slide 62: Day 2 Outline
Attack Process Revisited
Example: Garage Door
Example: Car Keys
Tool Setup
Q&A

## Slide 63: Attack Process Revisited
  Recall the high-level approach from Day 1:
Do we know the protocol in use?
Tool(s) available?
Run Attack
Develop Tool (if possible)
Identify or Deconstruct Protocol

## Slide 64: Attack Process Revisited
  Now we’ll broaden the approach by moving beyond common protocols and readymade tools…
Do we know the protocol in use?
Tool(s) available?
Run Attack
Develop Tool (if possible)
Identify or Deconstruct Protocol

## Slide 65: Extending Capabilities
Day 1 introduced common protocols and their specific tools
As these protocols evolve or phase out of use, software tools go unmaintained, hardware becomes obsolete, and certain techniques becomes less practical “in the wild”; examples:
  ApiMote, RZ Raven hardware (Zigbee)  obsolete
  Writeable GATT characteristics (Bluetooth)  vulnerability now uncommon
  Zniffer utility (Z-Wave)  unmaintained
Skilled wireless hackers focus on core elements that don’t change:
  Basic RF concepts
  How to assess/understand new protocols
  How tools are developed, modified, or chained
  Designing fuzzers, injectors, jammers, etc.
  (Building-blocks for the tools & frameworks we’ve seen up to this point)

## Slide 66: Extending Capabilities
For digging deeper, a more practical set of tools is needed
These typically form the “building blocks” of common tools and frameworks:
  Python (most open-source RF tools utilize python-based modularity)
    Scapy, Cryptography, Matplotlib, etc.
  SDR
    GNU Radio
      osmocom, scapy-radio, etc.
      Custom flowgraphs/plots
    Compatible Receivers/Transmitters
  Other tools/resources
    Published protocols
    Modular fuzzing platforms
    Wordlists, monitors, jammers, etc.

## Slide 67: Scapy
Many wireless hacking tools built using Scapy: https://scapy.net/
Combines with:
  Python modules like cryptography/matplotlib
  Community of open-source libraries, protocol definitions, etc.
  SDR tools (see next slide)
Recall ‘zbscapy’ from killerbee framework!

## Slide 68: Software-Defined Radio
Software-defined radio (SDR): radio communication system where components that conventionally have been implemented in analog hardware (e.g. mixers, filters, amplifiers, modulators/demodulators, detectors, etc.) are instead implemented by means of software on a personal computer or embedded system

## Slide 69: GNU Radio
Free software development toolkit that provides signal processing blocks to implement software-defined radios and signal processing systems
Can be used with external radio frequency (RF) hardware to create software-defined radios, or without hardware in a simulation-like environment
Widely used in hobbyist, academic, and commercial environments to support both wireless communications research and real-world radio systems

## Slide 70: GNU Radio
GNU Radio applications themselves are generally known as "flowgraphs", which are a series of signal processing blocks connected together, thus describing a data flow
Creates C++ or Python applications, can be modular/chained with other tools
Large community of open-source graphs, blocks, libraries etc. including:
  GR 802.11 projects
  GR Bluetooth stack
  Gr-lora block (LoRaWAN, LoRaPHY)
  Osmocom (osmocomBB, OpenBTS, etc.)
  Scapy-radio (see next slide)

## Slide 71: Scapy-radio
By Bastille Research: https://github.com/BastilleResearch/scapy-radio
Modified version of Scapy that can leverage GNU Radio to handle a SDR card
Includes flow & blocks written to handle several protocols:
  Bluetooth LE (advertising only)
  802.15.4 (used by Zigbee, Xbee, 6LoWPAN)
  ZWave (European frequency, 868MHz)

## Slide 72: GNU Radio: Examples
Wireless Measurement and Experimentation projects: https://www.wime-project.net/
Check out some of their advanced SDR projects
Useful protocol-based utilities all created with GNU Radio
Example shown on right: DIY Zigbee Transceiver

## Slide 73: GNU Radio: Examples
UL assessed the security of a medical device with a LoRa (“LoRaWAN”) RF module for long distance communication
Used Python to develop packet-decoder, fuzzer and jammer
HackRF One + GNU Radio used to imitate LoRa’s proprietary CSS-based modulation

## Slide 74: SDR: Compatible Hardware
Choosing an external radio: https://wiki.gnuradio.org/index.php/Hardware
Commonly used:
  RTL-SDR (~$10)
    Made from TV tuners; mostly Realtek RTL2832
    Integration via gr-osmocom
    Typical Range: 25 MHz ~ 1750 MHz
  YARD Stick One (~$125)
    Sub-GHz, half duplex
  HackRF One (~$350-400)
    Range: 1MHz to 6GHz
    Half-duplex transceiver
    Integration via gr-osmocom or gr-soapy
  Others: Lime SDR, Nuand BladeRF, Ettus USRP (>$1000)

## Slide 75: Radio Selection
  Protocol-based USB Dongles
    Pro’s
      Typically cheap, small
      Protocol-specific  Plug’n’play convenience
      Firmware often preinstalled
    Con’s
      Protocol-specific  quickly obsolete
      Dedicated Hardware, limited functionality
      Tedious to re-flash
      Proprietary RF modules limit control
      Compatibility issues
  Software-Defined Radio (SDR) Receivers/Transmitters
    Pro’s
      Good bandwidth
      Channels (Tx+Rx)
      Versatile (reusable) Hardware
      Can replace most dongles
      Build practical radio skills
      Complete control!
      Never obsolete
      One radio for all protocols…
    Con’s
      Mostly expensive
      Learning Curve
      Driver issues

## Slide 76: PHY Layer Demystified
We now understand the building blocks needed to develop tools for new/existing protocols
How do we identify or characterize radio communication when approaching a new or unknown protocol?
Must be familiar with basic, low-level RF concepts such as:
  Modulation
  Encoding (“Line Code”)

## Slide 77: Telecomm. Terms
Shaping of a signal to convey information
Vary properties of a periodic waveform (carrier signal) using separate signal containing transmitted data (message/modulation signal)
Many forms of modulation w/specific applications or strengths
“Keying” – representing digital message as analogue waveform (named after Morse Code)
Modulation

## Slide 78: Telecomm. Terms
Basic forms of digital modulation:
  Phase-shift keying
  Frequency-shift keying
  Amplitude-shift keying
  Quadrature amplitude modulation
All just different ways to represent bits!
With experience, RF hackers come to recognize common forms of modulation and their applications
Modulation

## Slide 79: Telecomm. Terms
Encoding is how we represent digital data sent via telecommunication
NOTE: “unipolar encoding” means essentially no encoding
  Carrier wave = binary 1
  No wave = binary 0
Short-distance RF devices often have data encoded, e.g., as Manchester code
  Bits represented by transitions
  More overhead, but better error detection
Again – will learn to recognize these and when/why they’re used
  Until then, keep visual reference handy!
Encoding (“Line Coding”)

## Slide 80: Telecomm. Terms
Example of Manchester encoded data:
Encoding (“Line Coding”)

## Slide 81: Common Protocols
Comparing RF Characteristics:
Note how these familiar protocols differ at the bottom layers of the protocol stack:
Technology | Band | Modulation | Encoding
BLE | 2.4GHz | GFSK | DSSS
Zigbee | 868/915MHz | BPSK | DSSS
 | 2.4GHz | OQPSK | 
Z-Wave | 868/915MHz | FSK | Manchester
LoRa | 868/915MHz | Proprietary CSS | ECC
Sigfox | 868/915MHz | DBPSK, GFSK | -
NFC | 13.56MHz | ASK | Manchester, Modified Miller

## Slide 82: Generic RF Attack Process
  Steps:
    Locate signal in RF band
    Capture/record signal for inspection
    Identify modulation scheme
    Identify encoding scheme
    Determine baud rate
    Extract/document symbols
    Reverse-engineer protocol format
  The following slides will explore how this process fits into a realistic attack scenario

## Slide 83: Day 2 Outline
Attack Process Revisited
Example: Garage Door
Example: Car Keys
Tool Setup
Q&A

## Slide 84: Example: Garage Door
Attack Scenario
To demonstrate the power of wireless attacks, consider the following scenario:
  Victim is leaving the house, and closing their garage door
  Attacker is nearby with a laptop and radio transceiver
  How can the attacker gain access to the victim’s garage (and possibly their residence)?

## Slide 85: Example: Garage Door
The attacker can utilize a replay attack, as shown on the right…
Let’s investigate the attacker’s process at a high level; by the end of this course, you will understand how to carry out such an attack
We’ll introduce some important concepts along the way
Attack Scenario

## Slide 86: Example: Garage Door
Where to start?
In this scenario, the attacker must ‘impersonate’ the RF transmission that opens the garage
Suppose the attacker can identify the victim’s garage remote – with a target device, where do we begin capturing RF signals?
To start, we must determine the frequency of the transmission we are capturing

## Slide 87: Example: Garage Door

## Slide 88: Example: Garage Door
FCC ID Lookup
In the US, devices which emit RF energy are regulated by the FCC
Any manufactured radio, remote, fob, smart-bulb, etc. must prove compliance
An FCC ID will be visible somewhere on the device and/or packaging
So – how does this help an attacker determine the frequency?

## Slide 89: Example: Garage Door
Attacker can look up the FCC ID to find a certification on the agency’s website
Details are publicly available!

## Slide 90: Example: Garage Door
Shown below is the result; by opening the “Exhibits”, the attacker will find detailed testing reports
Try looking this up as a quick exercise – click both Detail/Summary links to see the various graphs and specifications!
Information available will vary by product…
FCC ID Lookup

## Slide 91: Example: Garage Door
In this case, what the attacker needs is already displayed
Attacker has “located” target signal on the radio band…
  Alternatively, one could utilize spectral analysis (frequency scanning) to locate a transmission of interest
  RF hackers will anticipate common frequencies/bands based on target device; will vary based on geography!
Determining Frequency

## Slide 92: Example: Garage Door
Knowing the target band, attacker can now capture and inspect the victim’s RF transmission
Day 2 we will study these tools & techniques in detail
Signal Deconstruction

## Slide 93: Example: Garage Door
With a clear look, attacker recognizes modulation as “On-Off Keying”
(To extract raw data, an attacker must separate message & carrier signals)
Modulation

## Slide 94: Example: Garage Door
OOK is the simplest form of ASK (Amplitude-Shift Keying)
  Turning a transmitter On/Off, like Morse code
  Very common in short-distance communication
As with frequency, RF hackers will recognize common forms of modulation and their applications
Modulation

## Slide 95: Example: Garage Door
Attacker “demodulates” signal and extracts the raw digital data
By inspection, attacker can see that “unipolar” encoding (line code) is used
See encodings on next slide for reference…
Encoding

## Slide 96: Example: Garage Door
From one ‘click’ of the victim’s remote, our attacker now knows:
  Tx frequency, modulation, encoding
  Clocking/baud rate
  Burst/Command structure  raw Tx data
Attacker has effectively reverse-engineered the remote’s proprietary RF protocol
Documenting Protocol

## Slide 97: Example: Garage Door
As stated, the attacker in this scenario can simply play the initial recording using their own radio to open the garage
This would be the standard “replay attack”
As we’ll see later, real wireless attacks often require going further:
  Reversing/deconstructing protocol
  Crafting or modifying transmissions
Replaying Signal

## Slide 98: Example: Garage Door
Having deconstructed the transmission, the attacker could also recreate it using basic Software-Defined Radio (SDR) tools
We’ll learn to do this as well using GNU Radio
Will explore why these techniques are required for attacks (or testing!)
Crafting From Scratch

## Slide 99: Example: Car Keys
Suppose the attacker from Scenario 1 wants control of the victim’s car in addition to the garage
Can apply the same techniques from previous attack

## Slide 100: Example: Car Keys
Real example:
  Jaguar XK8 (1998)
  Frequency: 315MHz
    Labeled on remote; could also look up FCC ID
    Common for key fobs – again, RF hackers will come to know common frequencies
  OOK (ASK) modulation again

## Slide 101: Example: Car Keys
Real example:
  Hyundai Sonata (2012)
  Frequency: 315MHz
    Same as first example
  Modulation: This one uses Frequency-Shift Keying (FSK)
  Encoding: Manchester
  (Can you see how the modulation/encoding are evident in the images below?)

## Slide 102: Example: Car Keys
Suppose the attacker from Scenario 1 wants control of the victim’s car in addition to the garage
Can apply the same techniques from previous attack … sometimes!!!

## Slide 103: Example: Car Keys
The replay attack shown will not work for certain (generally, newer) key fobs, as security is improving
Day 3 will look at how this attack is mitigated, and how current defenses can in turn be bypassed…

## Slide 104: Day 2 Outline
Attack Process Revisited
Example: Garage Door
Example: Car Keys
Tool Setup
Q&A

## Slide 105: Tool Setup
Required Hardware:
  Laptop running recent version of Linux (Ubuntu, Kali, etc.) – not provided
  ‘HackRF One’ by Great Scott Gadgets – should be provided
  Target Device(s)
    ZAP Remote + Outlets
    Should be provided

## Slide 106: Tool Setup
Required Software:
  GQRX
    used for waterfall plot & recording raw I/Q data
    Install with “sudo apt-get install gqrx-sdr”
  Inspectrum
    Visual inspection of captures & symbol extraction
    Install with “sudo apt-get install inspectrum”
  GNU Radio
    (GUI application called GNU Radio “Companion”)
    Processing tool for Software-Defined Radio (SDR)
    Install with:
      sudo add-apt-repository ppa:gnuradio/gnuradio-releases
      sudo apt-get update
      sudo apt-get install gnuradio

## Slide 107: Day 2 Outline
Attack Process Revisited
Example: Garage Door
Example: Car Keys
Tool Setup
Q&A

## Slide 108: Day 3

## Slide 109: Day 3 Outline
Target Device
  Product Overview
  Product Setup
  Transmission Frequency
Capture
  Receiver Setup
  Performing Capture
Signal Deconstruction
  Inspecting Recording
  Symbol Extraction
  Documenting Commands
Q&A

## Slide 110: Day 3 Outline
Target Device
  Product Overview
  Product Setup
  Transmission Frequency
Capture
  Receiver Setup
  Performing Capture
Signal Deconstruction
  Inspecting Recording
  Symbol Extraction
  Documenting Commands
Q&A

## Slide 111: Product Overview
ZAP Remote Outlet Switch
By: Etekcity
https://etekcity.com/collections/zap-series-plugs
“Enjoy full control of your outlets with the Etekcity Remote Outlet. When paired with a remote, you can control your outlets in the palm of your hand.”
Set of 2 Remotes + 3 Outlets
Pair single remote w/multiple outlets

## Slide 112: Product Setup
Make sure remote is paired w/outlet and works
(Optional) Plug in test device
  lamp/bulb, etc. helps facilitate PoC
Note that each button sends a different signal
To start, we’ll focus on 1-ON button

## Slide 113: Transmission Frequency
On the package (as well as the outlet labels) we can see the transmission frequency is labeled for us… no need for FCC ID lookup

## Slide 114: Day 3 Outline
Target Device
  Product Overview
  Product Setup
  Transmission Frequency
Capture
  Receiver Setup
  Performing Capture
Signal Deconstruction
  Inspecting Recording
  Symbol Extraction
  Documenting Commands
Q&A

## Slide 115: Receiver Setup
Plug SDR device into your USB port
Open terminal and run ‘gqrx’
GQRX should detect radio chipset and configure itself
  Hit ‘OK’/enter if device is correct
  (If not, select correct device from dropdown menu)

## Slide 116: Receiver Setup
As target transmits at 433.92MHz, we’ll set our receiver to 433.9MHz
  Note: internal synthesizer may interfere w/target signal if we capture at EXACT frequency

## Slide 117: Receiver Setup
This button opens the IQ recorder
Make sure device is running (hit Play button in main window)
When ready, stop and start capture using ‘Rec’ button

## Slide 118: Receiver Setup
Note output file names:
  Date/time
  Capture frequency
  Sample rate
Also note the output directory

## Slide 119: Performing Capture
To reiterate:
  Set frequency
  Start radio (Play)
  Open IQ recorder
  Hit ‘Rec’ to start
  Press “1 ON” button on remote
  Hit ‘Rec’ to stop

## Slide 120: Day 3 Outline
Target Device
  Product Overview
  Product Setup
  Transmission Frequency
Capture
  Receiver Setup
  Performing Capture
Signal Deconstruction
  Inspecting Recording
  Symbol Extraction
  Documenting Commands
Q&A

## Slide 121: Inspecting Recording
Open capture file with inspectrum:
  “$ inspectrum –r [samp_rate]”
  Sample rate must match our capture file!

## Slide 122: Inspecting Recording
Scroll to locate transmission
Zoom out to scroll quicker
Adjust Power min/max for clear visual

## Slide 123: Symbol Extraction
We can see simple OOK is used for modulation
Let’s try and extract the transmitted symbols…

## Slide 124: Symbol Extraction
Press “Enable cursors”

## Slide 125: Symbol Extraction
Drag the cursor edge to adjust width
Match cursor to 1 symbol (bit)
Note the changing baud (symbol) rate

## Slide 126: Symbol Extraction
Increase symbol number to cover several symbols
Zoom in and resize for accuracy

## Slide 127: Symbol Extraction
Precise symbol period is 171us
Keeping this rate/period, we’ll use the cursors to highlight symbols we wish to extract

## Slide 128: Symbol Extraction
Right-click to add amplitude plot (as modulation uses amplitude-shift keying)
  Note: if target used frequency-shift keying, we’d use a frequency plot, etc. (remember the Sonata key fob from Day 1?)

## Slide 129: Symbol Extraction
Drag red line to cover signal
Right-click amplitude plot to add threshold plot
Adjust Power min/max to configure threshold for clear samples

## Slide 130: Symbol Extraction
Right-click threshold plot and select “Copy to clipboard” to extract highlighted symbols

## Slide 131: Symbol Extraction
Note the transmission contains a number of “bursts”
Highlight one burst at a time and extract symbols; paste into a text editor for inspection

## Slide 132: Symbol Extraction
You should see something like this for each burst
Note there are 97 symbols per burst
Note the periods between bursts – how many symbols??

## Slide 133: Symbol Extraction
Alternative methods for symbol extraction:
  GNU Radio
    Manual demodulation
    Scope plot (visual)
  Python + matplotlib
  BinViz (https://github.com/CBrunsch/BinViz)
    Binary “Vizualizer” for GNU Radio
    GUI for easy inspection & selection

## Slide 134: Documenting Commands
To facilitate comparison, we’ll want to record and condense the extracted output

## Slide 135: Documenting Commands
Using python (or your preferred method) we can clean up the strings quickly

## Slide 136: Documenting Commands
Repeat the steps as shown until you’ve extracted/recorded all symbols
Deconstructing the entire transmission gives us the format shown below
  # of bursts will vary with each press
  If using different remote, your symbols may differ slightly…

## Slide 137: Day 3 Outline
Target Device
  Product Overview
  Product Setup
  Transmission Frequency
Capture
  Receiver Setup
  Performing Capture
Signal Deconstruction
  Inspecting Recording
  Symbol Extraction
  Documenting Commands
Q&A

## Slide 138: Day 4

## Slide 139: Day 4 Outline
Protocol Deconstruction
Replay Attack
  Setup
  Running the Attack
Anticipating Replay Attacks
Q&A

## Slide 140: Day 4 Outline
Protocol Deconstruction
Replay Attack
  Setup
  Running the Attack
Anticipating Replay Attacks
Q&A

## Slide 141: Protocol Deconstruction
So far we’ve deconstructed the signal from just one button (1 ON)
To reverse engineer the entire protocol, we’ll need other signals to compare
  On vs. Off
  Other devices
  Other remotes
Pair (or plug in) one additional device, programmed to button 2
Using our first transmission as a guide, capture/deconstruct the following signals:
  1 OFF
  2 ON/OFF
  ALL ON/OFF
  If working in groups, use different remotes for additional variable

## Slide 142: Protocol Deconstruction
Reverse engineering the full command set (for one remote at least), we can identify the format shown below (again, your remote may differ slightly…)
With the protocol understood, we can use this information next for replay attacks and transmission synthesis

## Slide 143: Day 4 Outline
Protocol Deconstruction
Replay Attack
  Setup
  Running the Attack
Anticipating Replay Attacks
Q&A

## Slide 144: Replay Setup
Open GNU Radio Companion using either CLI or desktop shortcut as shown:

## Slide 145: Replay Setup
With an empty flowgraph open, use the search button to locate blocks by name

## Slide 146: Replay Setup
Add the following blocks as shown:
  File source
  Osmocom sink
  (additional) Variable
  Multiply Constant
Double-click block to edit attributes

## Slide 147: Replay Setup
GNU Radio starts w/sample rate variable by default
Our 2nd variable will be frequency
Set to “433.92e6” as shown

## Slide 148: Replay Setup
Osmocom sink is our radio device
Set Ch0 Frequency using our new variable
(Samp_rate set by default)

## Slide 149: Replay Setup
File source is the recording we will “replay”
Select the first recording we made for the 1-ON command
Set repeat to No

## Slide 150: Replay Setup
Set Multiply Constant to ‘1’

## Slide 151: Replay Setup
For Options:
  Set your preferred title
  Leave output language as Python
  GUI: None
  Run: Run to Completion

## Slide 152: Replay Setup
Lastly, connect the blocks as shown below:

## Slide 153: Running the Attack
Save the flowgraph
(Make sure radio is plugged in & Device 1 is OFF)
Hit ‘Run’ button to replay the captured transmission…
Should see Device 1 switch on – success!

## Slide 154: Day 4 Outline
Protocol Deconstruction
Replay Attack
  Setup
  Running the Attack
Anticipating Replay Attacks
Q&A

## Slide 155: Anticipating Replay Attacks
Sequencing
  Many wireless transmissions use a counter (“sequence number”, “packet number”, etc.) to prevent replay
  If counter isn’t incremented, packet/signal is rejected
  May be able to bypass by crafting the expected packet/signal
    Finding such values requires understanding a protocol, hence Day 2’s lesson on deconstruction/reversing commands
    To modify signals or craft from scratch, we’ll learn transmission synthesis on Day 4

## Slide 156: Anticipating Replay Attacks
Other defenses include challenge-response transactions, use of “rolling” codes, etc.
Common in newer cars – recall Day 1 we learned some key fobs not vulnerable to simple replay
These can be bypassed as well…
  Ex: rolling codes  “Roll Jam” bypass

## Slide 157: Anticipating Replay Attacks
Roll-Jam Attack
  “Rolling code” prevents attacker from replaying same signal
  By adding a jammer, attacker intercepts signal AND prevents the “roll” simultaneously
  Just as with software, wireless attacks can often be combined/chained for creative impact…
  We’ll see how to design a signal jammer on Day 5

## Slide 158: Day 4 Outline
Protocol Deconstruction
Replay Attack
  Setup
  Running the Attack
Anticipating Replay Attacks
Q&A

## Slide 159: Day 5

## Slide 160: Day 5 Outline
Transmission Synthesis
Jammer Design
Virtual Remote
Q&A

## Slide 161: Day 5 Outline
Transmission Synthesis
Jammer Design
Virtual Remote
Q&A

## Slide 162: Transmission Synthesis
First flowgraph simply replayed a capture
Real radio hacking  synthesize the signal from scratch
  More practical, much more impressive
  We’ve already done the groundwork by deconstructing the signals & protocol
Once again, we’ll use the 1-ON command

## Slide 163: Transmission Synthesis
Begin w/previous flowgraph, we’ll just make some modifications

## Slide 164: Transmission Synthesis
Delete File Source and Multiply Const

## Slide 165: Transmission Synthesis
Add new blocks Vector Source and Repeat

## Slide 166: Transmission Synthesis
Add new Variable blocks ‘baud’ and ‘sps’

## Slide 167: Transmission Synthesis
Set baud rate as shown

## Slide 168: Transmission Synthesis
Set samples/second as shown

## Slide 169: Transmission Synthesis
Add additional variables BurstA and BurstB

## Slide 170: Transmission Synthesis
Set Burst A (command sequence) using the symbols captured earlier

## Slide 171: Transmission Synthesis
Set Burst B (STOP sequence) using the symbols captured earlier

## Slide 172: Transmission Synthesis
Configure repeat using ‘sps’ variable as shown

## Slide 173: Transmission Synthesis
Vector Source is a python variable representing the command we’ll send
See how we can easily rewrite our pseudo-command from earlier:

## Slide 174: Transmission Synthesis
Set Vector using your command structure as shown
Set Repeat to No

## Slide 175: Transmission Synthesis
Lastly, connect the blocks as shown below
Re-title your flowgraph and Save As (to avoid overwriting 1st flowgraph)

## Slide 176: Transmission Synthesis
Now we’re ready to test; same as before:
  (Make sure radio is plugged in & Device 1 is OFF)
  Hit ‘Run’ button to transmit your crafted signal
  Should see Device 1 switch on – success!

## Slide 177: Day 5 Outline
Transmission Synthesis
Jammer Design
Virtual Remote
Q&A

## Slide 178: Jammer Design
We can now control the device with our radio. How can we take control away from others?
Let’s develop a jammer for our target device…

## Slide 179: Jammer Design
Using either Replay or Synthesis, craft a transmission to turn OFF the device
This time, set Repeat to ‘Yes’ in your Source block
Now run the flowgraph and try turning the device on using the remote
If jammer is working, remote should be rendered useless

## Slide 180: Jammer Design
Jamming exercise #1:
  Jam only specific device
  i.e. block outlet #1, leave #2 operational
Jamming exercise #2:
  Jam ALL devices for given remote
  (Use ALL OFF command, naturally)

## Slide 181: Day 5 Outline
Transmission Synthesis
Jammer Design
Virtual Remote
Q&A

## Slide 182: Virtual Remote
You may have noticed our flowgraphs generate Python scripts & (optionally) QT GUI’s
Just for fun, we can combine GNU Radio with PyQt and create a GUI application to control the target device(s) using a virtual remote that sends our crafted signals
The code has been written for you – however, you may need to edit the hardcoded signals to match your remote!

## Slide 183: Virtual Remote
Download and unzip “virtual_remote.zip” (included with training materials)
“cd [path/to/]virtual_remote”
In same directory, run using: “python3 ./zap_ctl.py”
Virtual remote should pop up on desktop

## Slide 184: Virtual Remote
Try pressing buttons!
  All work (except 3 & 4; feel free to add these for additional practice)
  LED blinks when used
  Terminal output shows commands transmitted
By combining GNU Radio with python/scripting, we could also develop tools such as protocol analyzers, “fuzzers”, etc.

## Slide 185: Day 5 Outline
Transmission Synthesis
Jammer Design
Virtual Remote
Q&A